## Slide 1: How to work with this learning material
Power Point
The following power point presents ports and inland vessels. The slides are shortly described in the notes below and you can also find the link to the source if you need further information.
Reader
In addition to the power point presentation, you can also use the reader provided on our platform. It’s more detailed and could be used as a script.
Links
You can also find the sources of our presentation and reader in the links section of the relevant bundled teaching material.
Videos and exercises
There are also videos and exercises, which can be used additionally to this presentation. You can find these videos and exercises separately in the relevant bundled teaching material.
https://www.rewway.at/en/teaching-materials/bundles/ports-and-inland-vessels/

## Slide 2: Learning Objectives and Target Group
After working through this content, the learners know…
general information about freight transport, criteria for the choice of transport means and the importance of the modal shift.
Relevant terminology, a comparison between the transport modes truck, train and inland vessel.
Stakeholders, types and the importance of multimodal transports and examples for it.
Target group
Secondary schools
Vocational school students
University students to use as an introduction in logistics, inland navigation and multimodal transport.

## Slide 3: Inland Vessels as part of the transport chain
Notes: This set of slides compares the different modes of transport – train, truck and inland vessel - with each other.

## Slide 4: Warm-Up Inland Navigation as Part of the Transport Chain
Which transport modes do exist?
What are their advantages and disadvantages?
Source: https://pixabay.com/en/logistics-truck-freight-train-877566/
Who are the stakeholders of multimodal transport?
What is multimodal transport?
Which mode of transport has the highest share of the modal split in Europe?
Notes: The questions mentioned in the slide above can be used as a warm up exercise for the topic “inland navigation as part of the transport chain”. The aim is to discuss the questions in plenum with participants. Answers to the questions will be provided during the presentation. Therefore, the questions can be discussed again at the end of the presentation.
Discussion questions (5-10 Minute Discussion):
Which transport modes exist?
What are their advantages and disadvantages?
What is multimodal transport?
Which mode of transport has the highest share of the modal split in Europe?
Who are the stakeholders of multimodal transport?
Input- possible topics of discussion:
Modal Split
Comparison to other transport modes
  price
  speed
  sustainability
Which transport modes do exist?
Advantages of the modes of transport
Advantages of multimodal transport
Source: Manual on Danube Navigation p 184-192

## Slide 5: Agenda Inland Navigation as Part of the Transport Chain
Transport Mode Comparison
Multimodal Transport
Freight Transport
Transport Examples

## Slide 6: Freight Transport
transport = change of location of goods by means of transport (i.e. truck, train, maritime vessel or inland vessel)
freight transport is a prerequisite for commerce and industry  therefore it ensures our prosperity
increasing freight transport due to increasing globalisation and division of labour
freight transport contributes to our prosperity, but in reverse it is not allowed to become a reason for increasing burden on human and environment
Notes: Transport is defined as the change of location of goods by means of transport. There is a differentiation between in-house and external transport. External transport is carried out outside from buildings by using transport infrastructure and is also called freight transport. Means of transport are used for the transport of goods. Freight transport is a prerequisite for commerce and industry, thus it ensures our prosperity. Freight transport contributes to our prosperity, but in reverse it is not allowed to become a reason for increasing burden on human and environment. Freight transport and logistics therefore hold a key position in the design of transport systems.
Source: translated from German: Claußen, U. / Geiger, C.: Verkehrs- und Transportlogistik, Berlin-Heidelberg, 2013, S. 3ff.

## Slide 7: Freight Transport
suitable transport mode depending on the products characteristics, quantity, measures, location of consignor/consignee
situation-related transport planning required
a shift from truck to other means of transport is necessary, because:
  the capacity on roads is finite
  expansion possibilities on roads is finite
  lack of truck drivers
  increase of safety
  burden for the environment
  noise
Notes: An increase of transport performance has been forecasted for all modes of transport. Due to the finite capacities and expansion possibilities on roads it becomes essential to avoid traffic or to shift the traffic away from roads to other modes of transport. Besides of finite capacities on roads, also noise, climate-damaging emissions and land usage are increasing.
Source: translated from German: Claußen, U. / Geiger, C.: Verkehrs- und Transportlogistik, Berlin-Heidelberg, 2013, S. 3ff.

## Slide 8: Freight Transport in Europe
the proportion of inland waterway navigation is very different within the countries
  i.e. the Netherlands has important sea ports and an extensive inland waterway network  the highest share in the EU with 41,6 % in 2020
  i.e. Malta and Cyprus do not dispose over inland waterways at all, therefore the share is 0 %.
Chart: Modal Split EU-27 2020
| Straße | Schiene | Wasserstraße
Modal Split EU-27 2011: Binnenverkehrsträger in Millionen tkm | 1734 | 420 | 141
proportion of different transport modes
source: Eurostat
Notes: In the 27 countries of the European Union, waterways made up a 5.8 % share of the modal split in 2020 – which means that 5.8 % of all freight ton-kilometres were handled on waterways. This share differs sharply in the individual EU states. The Netherlands, for instance, have important seaports and a highly integrated inland waterway network which is divided into small sections. This results in the highest inland navigation share of the 27 EU countries (41.6 % in 2020).
Source: Manual on Danube Navigation page 21.
https://ec.europa.eu/eurostat/statistics-explained/index.php/Freight_transport_statistics_-_modal_split#Modal_split_in_the_EU

## Slide 9: Agenda Inland Navigation as Part of the Transport Chain
Transport Mode Comparison
Multimodal Transport
Freight Transport
Transport Examples

## Slide 10: Terminology Transport Mode Comparison
Means of transport: vehicles that serve to goods and passengers such as trucks, trains or inland vessels
Mode of transport: transport infrastructure (such as roads, rail, inland waterways,…)
Pre-haulage: partial route at the beginning of the transport chain (often by truck)
End-haulage: last part of the transport chain, to the recipient (often by truck)
Notes: There are several transport modes and means of transport. A transport mode provides the necessary infrastructure for using a certain means of transport. Road, rail and waterway are possible transport modes.
Means of transport are technical facilities and equipment for the transport of people and goods. Means of transport in freight transport are, for example, inland vessels, trucks and trains.
The first part of the transport chain is called pre-haulage and constitutes the delivery of a cargo to the first point of transhipment (such as a port). Pre-haulage is often carried out by truck.
The term main leg describes the transport of goods or loading units from the consignor‘s transhipment point to the consignee‘s transhipment point. The word „main“ results from the fact that the longest part of the transport is performed between these points.
End-haulage describes the delivery of the cargo from the consignee‘s point of transhipment to the consignee‘s location. Usually, end-haulage is carried out by truck.
Manual on Danube Navigation page 185-187

## Slide 11: Transport Mode Comparison
Indicators | Inland vessel | Train | Truck
transport time | usually longer (transhipment, pre-, end-haulage) | usually longer than per truck | usually shorter (often door-to-door-delivery)
capacity | 1 convoy with 4 pushed lighters (7.000 net tons)= | = 175 railway wagons | =280 trucks
punctuality aspects | high-/lowwater, ice formation | weather, accidents, construction sites | traffic jams, accidents, weather
safety | hardly any accidents | nearly no risk of accidents | highest risk of accidents
infrastructure | limited to navigable inland waterways | limited to railway network | best infrastructure
costs | depending on amount, distance and planning (advantage inland vessel: highest transport capacity per unit) |  | 
environmental aspects | lowest CO2-emissions and energy consumption (compared to transport quantity) | low energy consumption (compared to transport quantity) | highest energy consumption and CO2-emissions
Notes: Source: Manual on Danube Navigation p 18-20
Further information on the different aspects will be given within the next slides.

## Slide 12: Transport Capacity Transport Mode Comparison
transport capacity: 1 pushed convoy with 4 pushed lighter = 175 railway wagons = 280 trucks = 20 km convoy of trucks
Notes:   Compared to other land transport modes, Danube navigation offers a significantly higher transport capacity per transport unit. For instance, a single convoy with 4 pushed lighters can transport around 7,000 t of goods – equivalent to the cargo carried by 175 railway wagons (with 40 net tons each) or 280 trucks (with 25 net tons each). Hence, increasing cargo transport on the Danube means a significant reduction in congestion, noise emissions, environmental pollutions, road accidents and the burden of the rail system.
  Picture: Manual on Danube Navigation page 19.
  Source: viadonau, Manual on Danube Navigation page 18,19.

## Slide 13: Energy Consumption Transport Mode Comparison
specific energy use:
an inland vessel is able to transport one ton of cargo almost four times further than a truck using the same consumption of energy
Notes:   In regard to specific energy consumption, inland navigation can be described as the most efficient and hence environmentally friendly transport mode. Inland vessels can transport one ton of cargo almost four times as far as a truck with the same energy consumption.
  Source: Manual on Danube Navigation page 18.
  Picture: viadonau, Manual on Danube Navigation page 18.

## Slide 14: External Costs Transport Mode Comparison
inland vessels cause the lowest costs of accidents, noise, air pollution and climate
Notes:   Inland navigation also accounts for the lowest external costs, so those costs associated with climate gases, air pollutants, accidents and noise. CO2 emissions are comparatively low in particular, which means that inland navigation can contribute to achieving the European Union climate targets.
  Source: Manual on Danube Navigation page 18.
  Picture: PLANCO Colsulting & Bundesanstalt für Gewässerkunde 2007, Manual on Danube Navigation page 19.

## Slide 15: Safety, Availability, Infrastructure Costs Transport Mode Comparison
inland vessels as safest transport mode:
  only 12 traffic accidents on the Austrian-Danube in 2021 (no cases of death)
availability around the clock: no bans on weekend- and night driving
low infrastructure costs: natural infrastructure is usually available -> low costs
improving the complete infrastructure of the Danube waterway would require an investment of € 1.2 billion. This corresponds roughly with the cost of constructing 50 km of road or rail infrastructure.
Notes: In 2021, there were a total of 12 traffic accidents involving inland vessels on the Austrian Danube, and no fatalities were recorded.
As in most cases it is possible to make use of the inland waterways as natural infrastructure, thus infrastructure costs are quite low.
Current costs estimates of infrastructure projects in the riparian states suggest that improving the whole infrastructure of the 2,415km Danube waterway would cost 1.2 billion Euros in total. This is more or less equivalent to the costs of constructing around 50km of road or rail infrastructure. Current European rail tunnel projects each cost 10 to 20 billion Euros.
The right picture shows the comparison of infrastructure costs, on an example of German inland transport modes. The inland vessel with 12.6 Euros per 1000 ton-kilometres is the lowest of all three modes.
Source: Annual Report on Danube Navigation 2021, p 2
(http://www.viadonau.org/en/newsroom/publications/folders/ )
Manual on Danube Navigation page 19,20
Picture: PLANCO Colsulting & Bundesanstalt für Gewässerkunde 2007, Manual on Danube Navigation p 19

## Slide 16: Strengths/Weaknesses Inland Vessel Transport Mode Comparison
low transportation costs
bulk freight capacity
environmental friendliness safety availability around the clock low infrastructure costs
dependence on variable fairway conditions low transport velocity low network density, often requiring pre- and end- haulage
source: based on viadonau.
Notes: The principal strengths of Danube navigation are the ability to transport large quantities of goods per vessel unit, its low transport costs and its environmental friendliness. Furthermore, it is available around the clock, with no prohibition on driving at weekends or during the night and can provide a high degree of safety and low infrastructure costs.
The weaknesses lie in its dependence on fluctuating fairway conditions and the consequent, varying degree of the vessel load factor, the low transport speed and network density, which often necessitate pre- and end-haulage by road or rail.
Manual on Danube Navigation page 17.
Picture: based on Manual on Danube Navigation page 17.

## Slide 17: Opportunities/Threats Inland Vessel Transport Mode Comparison
spare capacity of the waterway
rising demand for green transport modes
modern and harmonised cross-border information services (RIS)
cooperation activities with road and rail
international development initiatives (e.g. NAIADES, Strategy for the Danube Region)
inadequate maintenance of the waterway in some Danube riparian countries
Administrative barriers lead to competitive disadvantages
high requirement for modernisation of ports and fleets
source: based on viadonau.
Notes: The opportunities of Danube navigation are the high free capacities of the waterway, international development initiatives such as the strategy for the Danube region, the internalisation of external costs at European level, cooperation with road and rail, as well as the use of modern and harmonised River Information Services (RIS).
The threats to Danube Navigation are found in the different political and hence budgetary importance assigned to this transport mode in the individual Danube states, as well as in the need to modernise many Danube ports and parts of the Danube fleet.
Manual on Danube Navigation page 17.
Picture: based on Manual on Danube Navigation page 17.

## Slide 18: Agenda Inland Navigation as Part of the Transport Chain
Transport Mode Comparison
Multimodal Transport
Freight Transport
Transport Example

## Slide 19: Involved Stakeholders Multimodal Transport
consignor – a person, giving away the freight to be delivered
consignee – person to whom the freight is to be delivered
forwarder – organises the transport – intermediate between consignor and carrier
carrier – responsible for the transport
terminal(operator) – responsible for the transhipment of goods
Notes: There are many involved stakeholders in a multimodal transport chain. The following stakeholders are the most important ones in a multimodal transport chain:
The consignor, or sender, is the person who passes the goods on to the next stakeholder in the transport chain. Consignors could be producers of goods for example.
The consignee, or the receiver, is the person who has the right to receive the goods on its destination.
The forwarder organises the transport and further services as an intermediately on behalf of the consignor.
The carrier is responsible for the freight transport itself. The carrier provides the means of transport, the forwarder only organised the transport.
A terminal provides facilities for an efficient transhipment process, which is carried out by terminal employees.
Shipping companies organise and carry out transports. For the transports own and foreign ships are used.. Shipping companies also prepare and monitor the transports on land.
Source: translated from German: Handbuch Intermodaler Verkehr, 2010, S. 36ff.

## Slide 20: Multimodal Transport
definition:
  transport of goods using two or more means of transport
advantages and usage:
  optimized combination/usage of vessel, train and truck
  often used for long-distance and time flexible transport -> transhipment = time = money
  cheaper and environmentally friendly
Notes: Multimodal transport is characterised by the transport of goods using two or more different transport modes (e.g. change from waterway to rail). In order to change the means of transport, transhipment of the goods is required. In doing this, the strength of the several individual transport modes can be used and the cheapest and environmentally friendly combination can be chosen. Since each transhipment involves additional time and causes additional cost, multimodal transport is often used for long-distance transport where delivery time is not an important factor.
Manual on Danube Navigation page 186.
Picture: Günthner 2001, Manual on Danube Navigation page 186.

## Slide 21: Multimodal Transport
split transport
  transport with at least two transport means/modes
  cargo itself is transhipped
  e.g. liquids, machinery…
intermodal transport
  transport with at least two transport means/modes
  only loading units – not the cargo itself is transhipped
  e.g. container transport
combined transport
  special type of intermodal transport
  major part by vessel or train
  pre- and end-haulage carried out by truck is minimized
Source: Garant-Tiernahrung Gesellschaft mbH
Notes: In split transport, two or more different means of transport or transport modes are used and the cargo itself is transhipped. This is the main difference compared to intermodal transport: in the latter case, it is not the cargo itself, but only the loading units(including cargo) that are transhipped. This means that, when changing transport means, only the loading units or the road vehicles are switched, while the goods remain in the same transport receptacles (such as containers or swap bodies). Since only loading units or the road vehicles are reloaded, this method saves cost and time.
Combined transport is a special type of intermodal transport in which the major part of the trip is performed by inland vessel or railway and any pre- and/or end-haulage carried out by truck is minimised. When rail or waterway transport is used for the main leg, combined transport represents an environmentally friendly transport alternative.
Manual on Danube Navigation page 187-188
Picture: Garant-Tiernahrung Gesellschaft mbH, Manual on Danube Navigation p 95

## Slide 22: Overview Multimodal Transport
multimodal transport
intermodal / combined transport
subdivided transports
subdivided
bulk transport
Goods are individualized and distinguishable E.g.: pallet
general cargo transport
Goods are indistinguishable
E.g.: liquid goods, gravel
The goods are reloaded on different means of transport
Total freight transport takes place in the same loading unit / road vehicle
Notes: Concerning subdivided transports there is also a distinction between subdivided bulk transport and general cargo transport.
In the case of subdivided bulk transport goods are transported unpackaged, since bulk goods can not be transported piecewise, they are measured in units of measurement, e.g. tons or liters. Examples include liquid cargo such as oil, bulk goods such as coal or ore and suction material such as grain. Regarding general cargo transport, goods are transported which are individualized and distinguishable. The goods can be handled individually, with the stock indicated in number of pieces. Examples are machines or pallets.
Source: Manual on Danube Navigation p 187, 188

## Slide 23: Importance Multimodal Transport
increasing cargo volumes due to internationalisation of production activities and high level of consumption
increasing cargo volumes also due to the trend towards a minimisation of warehousing
A shift towards more environmentally friendly transport modes is absolutely necessary, to reduce congestion on roads, noise and CO2 emissions.
problem-solving approach: promoting multimodal and in particular combined transport
s
Notes: A 2015 study by the European Commission predicts that cargo transport volumes in the 28 states of the European Union will rise by 1.6% each year between 2020 and 2030. The reasons for the predicted sharp rise in cargo transport volume lie with the internationalisation of production activities and the high level of consumption in Europe. Another reason for an increase in traffic volume is the trend towards a minimisation of warehousing in order to cut costs. In order to minimise the negative results of rising traffic volumes on society and the environment, a shift towards more environmentally friendly transport modes such as waterways and rails is absolutely necessary. This shift can reduce negative results such as noise or CO2 emissions significantly. An improvement of the situation can be subsequently achieved by multinational transport solutions, i.e. the ideal combination of vessels, rails and trucks.
Source: Manual on Danube Navigation, p 184

## Slide 24: Multimodal Transport
reasons to carry out multimodal transports:
environmental aspects,
location and
lack of truck capacities
profitability – key factors:
efficient transhipment
cost reduction for pre- and end-haulage
compensation of additional expenses by bundling the main leg
offering value-added logistics services
Notes: The requirement of logistics and transport services increased strongly in the past. More and more goods are shipped in small consignments. Due to the finite capacities and expansion possibilities on roads it becomes essential to avoid traffic or to shift the traffic away from roads to other modes of transport. Besides of finite capacities on roads, also noise, climate-damaging emissions and land usage are increasing.
The choice of means of transport is dependent on different influencing variables. The advantages and disadvantages of the different means of transport are also expressing themselves through the transport price. Thus the transport price is not the only decision criteria for the means of transport. The amount and the measures of the goods, as well as the location of consignor/consignee and the quality of transport are important for the choice of the appropriate means of transport.
Source: translated from German: Claußen, U. / Geiger, C.: Verkehrs- und Transportlogistik, Berlin-Heidelberg, 2013, S. 3ff.

## Slide 25: Promotion of Combined Transport Multimodal Transport
EU-Directive to liberalise pre- and end-haulage of combined transport
raise attractiveness of combined transport by:
  simplifying cross-border transport
  benefits concerning road vehicle tax (e.g. exemption from tax)
  financial subsidies
  other advantages: exceptions to the bans on night-time driving, weekends and public holiday, etc.
Notes: Numerous transport policy measures have been taken to encourage the use of combined transport. This is aimed at guaranteeing an early shift towards environmentally friendly modes of transport – meaning a shift from truck to ship or railway. Ways of achieving the enforced use of combined transport consist of various funding schemes on a national and international scale as well as fiscal and regulatory measures.
Also the European Union has taken an important step towards an increase in usage of combined transport. The EU Directive concerning the establishment of common rules for certain types of combined transport of goods between member states was implemented in Austria with the Regulation on the exemption of cross-border combined transport from the approvals procedure.
Manual on Danube Navigation page 200-201.

## Slide 26: Agenda Inland Navigation as Part of the Transport Chain
Transport Mode Comparison
Multimodal Transport
Freight Transport
Transport Examples

## Slide 27: Multimodal Transport of Fertilisers
fertilisers: transport in Big Bags (see picture)
type of transport: multimodal transport
maritime vessel: Rouen (FR) - Constanta (RO)
inland vessel: Constanta (RO) – Bulgaria/Serbia/Hungary/Romania
transhipment from maritime to inland vessel by floating cranes.
Source: Borealis L.A.T.
Notes: Borealis L.A.T. produces nitrogen fertilisers and technical nitrogen products at several locations in Europe.
Vessels with a loading capacity up to 15,000 t can dock and tranship at the company‘s quay. Some of the ammonium nitrate production is transported to Constanta by maritime vessel and transhipped directly to inland vessels by floating cranes.
These vessels then supply the distribution warehouses in Bulgaria, Serbia, Hungary and Romania.
Transporting products right across western Europe is difficult, as ammonium nitrate is classified as class 5.1. dangerous good and transport by lighters is not always possible in cases of low water.
Source: Manual on Danube Navigation page 194
Picture: Borealis L.A.T., Manual on Danube Navigation page 194

## Slide 28: Multimodal Transport of Steel Products
voestalpine:
own factory port
steel products (= general cargo) worldwide transport – partly by vessel:
  transhipment in a covered transhipment hall in Linz
  transport of 500.000 tons of steel/year to Moerdijk (near Rotterdam)
  in Moerdijk transhipment onto maritime vessels
  destinations: USA, Brazil, India,…
  end-haulage via train and truck
Source: Industrie-Logistik_Linz (ILL)
Source: Industrie-Logistik_Linz (ILL)
Notes: Each year, 500,000 tons of steel are transported via inland vessels on the route from Linz to Moerdijk. The steel products are collected by railway wagons form several warehouses on the company complex. Following this, they are transported to a covered transhipment hall which is located at the private port of voestalpine in Linz. There, the goods are directly transhipped from the wagons onto inland vessels. For this covered transhipment, a gantry crane with a maximum capacity of up to 35 tons is used. Subsequently, the goods are transported to Moerdijk by pushed convoy. There, the goods are transhipped to maritime vessel and then transported to seaports located near the final customer. The latter are located in countries such as Brazil, the U.S., Singapore, India, Malaysia or South Africa. In most cases, the end-haulage is done by railway, though sometimes by trucks.
Manual on Danube Navigation page 198.
Pictures: Industrie-Logistik-Linz (ILL) Manual on Danube Navigation 198

## Slide 29: Multimodal Transport of Concrete Segments
Rhenus Donauhafen Krems:
concrete segments (tower parts) for wind turbines
export to Germany from Krems and Bad Deutsch-Altenburg
per inland vessel = transport of a whole tower (consisting of 50 parts)
preventing 50 special transport by road
Quelle: Rhenus Donauhafen Krems
Notes: Concrete tower segments for wind parks have been transhipped at the Krems site since 2011. Here, the port of Krems teams up with the company Prangl as part of a cooperative project. Produced in Northern Germany, the concrete segments were, in the initial years, transported in complete ship loads to Krems, where Rhenus unloaded the vessels, placed segments in storage and then loaded them onto trucks for onward transport. The Rhenus Donauhafen Krems has a warehouse and crane capacity for this purpose that is unrivalled elsewhere on the Danube. Later on the customer built a factory in Austria; this turned what had previously been imports from Germany to Austria into export of the concrete to Germany.
Since mid 2012, transhipment has been ongoing for the same manufacturer at a special viadonau transhipment site in Bad Deutsch-Altenburg. Prangl supports Rhenus with a 400-ton crawler crane and also conducts pre- und end-haulage.
More than 4,000 segments were loaded in Krems and Bad Deutsch-Altenburg in 2017 alone, whereby the majority of inland shipping transports were conducted by Rhenus Danube Shipping. A complete tower, consisting of 50 parts, can be transported in a single vessel, thus preventing 50 special transports by road.
Manual on Danube Navigation page 196
Pictures: Rhenus Donauhafen Krems, Manual on Danube Navigation 196

## Slide 30: Multimodal Transport of Mineral Raw Materials
Ennshafen:
mineral raw materials = bulk cargo
very sensitive to moisture –> difficult to transport
via maritime vessel to Rotterdam
transhipment to inland vessels in Rotterdam
via Rhine, Main and Main-Danube-Canal to Ennsdorf
unloading in Ennsdorf using cranes and wheel loaders
Source: LITHOS Industrial Minerals GmbH
Source: LITHOS Industrial Minerals GmbH
Notes: The company LITHOS Industrial Minerals GmbH received a consignment of raw materials by inland vessel in November 2017. 6,000 t of talc stone were loaded on maritime vessel in Asia and transhipped to inland vessels in Rotterdam. Transport from Rotterdam to Ennsdorf took roughly two weeks.
The vessels were unloaded using crane and two wheel loaders in cooperation with the neighbouring transhipment company Fuchshuber Agrarhandel GmbH. Employees at the Ennshafen were responsible for weighing the inland vessels. LITHOS replenished all of its stock with this single raw material delivery.
The entire fulfilment process was monitored and checked by LITHOS employees. They were on site during every important event along the transport route. Unloading the inland vessels and transport by wheel loader took approximately one week.
Manual on Danube Navigation page 193
Pictures: LITHOS Industrial Minerals GmbH, Manual on Danube Navigation page 193

## Slide 31: Cross word Final Exercise
create a cross word (an instruction sheet and a solution sheet) and change it with your colleagues, so that everyone is solving another cross word.
for the questions of the cross word, you can use all information given within this presentation.
do not forget to mention if the solutions should be introduced vertically or horizontally within the cross word.
Notes: This exercise is suitable as an individual exercise.
Duration: 30-40 minutes

## Slide 32: Internet Research Final Exercise
search on the internet for facts and figures about the modal split in the EU
analyse the relative importance of the different inland transport modes (road, rail, inland waterways) in freight transport in the European Union (EU)
create a PowerPoint, a flipchart, a Prezi, etc.
Notes: This exercise is suitable as an individual or group exercise (max. 3 participants)
Duration: 20-30 minutes.

## Slide 33: Sources
viadonau (2020): Manual on Danube Navigation, Vienna.
Order or download: http://www.viadonau.org/en/newsroom/publications/manual-on-danube-navigation/
viadonau (2021): Danube Navigation in Austria– Annual Report 2021, Vienna. Download: http://www.viadonau.org/en/newsroom/publications/folders/
INeS Danube information platform on intermodal inland navigation Homepage: http://www.ines-danube.info/?lang=en
Posset, Gierlinger, Gronalt, Peherstorfer, Pripfl, Starkl (2014): Intermodaler Verkehr Europa, Wien. Order at: http://www.logistikum.at/forschung/verkehrslogistik/intermodaler-verkehr-in-europa/kontaktbestellung.html

## Slide 34: Further Information
We hope our set of slides has met your expectations!
- you are free to use, adapt and share this slides and to use it for your lectures.
For questions and feedback please do not hesitate to contact us:
rewway@fh-steyr.at
Further set of slides are available at:
http://www.rewway.at/en/teaching-materials/bundles/
Maybe you are interested in booking a Transport School Lab,
a guest lecture or an excursion?
http://www.rewway.at/en/services/